## Slide 1: Becker
U5.
Oil lubricated rotary vane pumps

## Slide 2: German made
oil lubricated rotary vane pumps
Five frame sizes 70-360 m3/h
Fastest pump-down times
Fastest reaching of ultimate pressure
    Even after cold starting
Low power consumption
    Hygienic Design
    Smooth surfaces for quick. easy and hygienic cleaning
    Compact dimensions
O2-PACK
    Version for oxygen – same length as standard version
VARIAIR
    Intelligent frequency inverter with additional features

## Slide 3: U5.
for a variety of applications
Food packaging
Food processing
    Tumblr
    Dry freezing
    Vacuum mixer/ Sausage machinery
Degassing of materials (electronics, food …)
Medical central systems
Thermoforming
Rubber molding
Drying of materials or parts
CNC router tables
(Reflow) Soldering
Lamination of materials
And many more

## Slide 4: U5.
Design / Concept

## Slide 5
U5.
design / concept

## Slide 6: U5.77/101
design / concept
Air guidance and oil return are integrated into the side covers/ lids

## Slide 7: U5.166/201/301
design / concept
Air guidance and oil return are integrated into the side covers / lids

## Slide 8: U5.
design / concept
71-201 share the same elements
71/101
166/201
301

## Slide 9: U5.71/101
Standard (Diverting cap)
Optional (Female thread
and burst valve)
exhaust connection

## Slide 10: U5.71/101
Standard (Diverting cap)
Optional (Female thread
and burst valve)
exhaust connection

## Slide 11: accessories
U5.166/201/301 with standard covers
U5.166/201/301 Optional covers Female thread with burst valve
Exhaust
air
Oil sight glass for oil check (min/max)
Oil inlet
Oil drain screw; oil outlet
Oil level switch (or plug)
Oil temperature monitor
Plug or maintenance indicator for oil separating elements
U5.
Optional: Service cover with different options

## Slide 12: gas ballast valve
U5.71 & U5.102
  Fixed gas ballast valve <1 mbar as standard
  Adjustable optional gas ballast valve <3 mbar for moist applications
U5.166-301
  Adjustable gas ballast valve <1 mbar as standard
  Adjustable optional gas ballast valve <3 mbar for moist applications
Ultimate vacuum without gas ballast valve <0.1 mbar
U5.

## Slide 13: external
Smooth surfaces
  Reduction of deposits in potential nests
Corrosion resistance
  All U5. pumps are lacquered
Wash-down capable
  IP55
U5.

## Slide 14: U5.
accessories and systems
Broad range of external accessories
Inlet filters
Water separators
Tank systems
Cables
Etc.

## Slide 15: U5.
XL version
U5.71 – 301 XL versions for rough vacuum applications
Key benefits
  Better oil separation
    Longer oil tank (twice the length) => better separation because of gravity
    Additional separating element => better oil recovery
    Heavy air flow protection for the float chamber => less risk of oil carry-over
    Longer service intervals
      Additional separating element => better oil recovery
      Increased surface => better cooling capabilities

## Slide 16: U5.300
XL

## Slide 17: U5.
XL

## Slide 18: U5.
XL oil separation
Standard U5.300

## Slide 19: U5.
XL additional oil separation stage

## Slide 20
O2-PACK
Suitable for oxygen
  Fomblin-oil
  BAM conform materials
Same length as standard U5.
  Even though there is an additional internal oil separator
  No external oil separator
3-time separation
  Coarse separator
  Oil separator element
  Additional separator
Versions
  U5.71-301
U5.

## Slide 21: vs. R5 RA 63F
Construction size | U5.71 | R 5 RA 63 F
Length [mm] | 696 (IE3) | 627 (IE2)
Width [mm] | 380 | 406
Height [mm] | 289 | 290
Mass [kg] | 67 | 55
Nominal pumping speed [m³/h 50/60 Hz] | 70/84 | 63/76
Motor power [kW – 50/60 Hz] | 1.5/1.8 | 1.5/1.8 2.2/2.7
Noise level [dB(A)] | 64/67 | 64/67
Becker U5.71

## Slide 22: vs. R5 RA 100F
Becker U5.101
Construction size | U5.101 | R 5 RA 100 F
Length [mm] | 736 (IE 3) | 701 (IE 2)
Width [mm] | 380 | 406
Height [mm] | 289 | 290
Mass [kg] | 67 | 73
Nominal pumping speed [m³/h 50/60 Hz] | 100/120 | 100/120
Motor power [kW – 50/60 Hz] | 2.2/2.6 | 2.2/2.7 2.7/3.4
Noise level [dB(A)] | 65/68 | 65/68

## Slide 23: vs. R5 RA 160 D
Becker U5.166
Construction size | U5.166 | R 5 RA 160 D
Length [mm] | 810 | 920
Width [mm] | 510 | 536
Height [mm] | 360 | 410
Mass [kg] | 99 | 140
Nominal pumping speed [m³/h 50/60 Hz] | 165/198 | 160/190
Motor power [kW – 50/60 Hz] | 3.0/3.6 | 4.0/5. 5
Noise level [dB(A)] | 70/72 | 70/72

## Slide 24: vs. R5 RA 202 D
Becker U5.201
Construction size | U5.201 | R 5 RA 202 D
Length [mm] | 789 | 920
Width [mm] | 510 | 536
Height [mm] | 360 | 410
Mass [kg] | 102 | 140
Nominal pumping speed [m³/h 50/60 Hz] | 200/240 | 200/240
Motor power [kW – 50/60 Hz] | 4.0/4.8 | 4.0/6.6
Noise level [dB(A)] | 72/74 | 72/74

## Slide 25: vs. R5 RA 302 D vs. R5 RD 360
Becker U5.301
Construction size | U5.301 | R 5 RA 302 | R5 RD 360
Length [mm] | 946 | 1011 | 990
Width [mm] | 549 | 581 | 530
Height [mm] | 365 | 410 | 410
Mass [kg] | 143 | 190 | 190
Nominal pumping speed [m³/h 50/60 Hz] | 300/360 | 300/360 | 300/360
Motor power [kW – 50/60 Hz] | 5.5/6.6 7.5/9.0 | 5.5/6.6 7.5/9.0 | 5.5/6.6 7.5/9.0
Noise level [dB(A)] | 73/76 | 74/76 | 70/72

## Slide 26: vs. U4.300 vs. U4.250
Becker U5.301
Construction size | U5.301 | U4.300 | U4.250
Length [mm] | 946 | 1075 | 1097
Width [mm] | 549 | 533 | 531
Height [mm] | 365 | 418.5 | 385
Mass [kg] | >143 | >145 | >145
Nominal pumping speed [m³/h 50/60 Hz] | 300/360 | 300/360 | 244/276
Motor power [kW – 50/60 Hz] | 5.5/6.6 7.5/9.0 | 5.5/6.6 7.5/9.0 | 5.5/6.6 7.5/9.0
Noise level [dB(A)] | 73/76 | 74/76 | 73/76

## Slide 27: vs. R5 RA 0063 F
Becker U5.71

## Slide 28: vs. R5 RA 0063 F
Becker U5.71

## Slide 29: vs. R5 RA 0100 F
Becker U5.101

## Slide 30: vs. R5 RA 0100 F
Becker U5.101

## Slide 31: vs. R5 RA 0160 D
Becker U5.166

## Slide 32: vs. R5 RA 0160 D
Becker U5.166

## Slide 33: vs. R5 RA 0202 D
Becker U5.201

## Slide 34: vs. R5 RA 0202 D
Becker U5.201

## Slide 35: vs. R5 RA 0302 D
Becker U5.301

## Slide 36: vs. R5 RA 0302 F
Becker U5.301

## Slide 37: vs. U4
Becker U5.301

## Slide 38: vs. U4
Becker U5.301

## Slide 39
motor power
Volume | Becker U5. (50/60Hz) | Busch R A R5 (50/60Hz)
70m³/h | 1.5/1.8 | 1.5/1.8 2.0/2.7
100m³/h | 2.2/2.6 | 2.2/2.6 2.7/3.4
165m³/h | 3.0/3.6 (4.0/4.8) | 4.0/5.5
200m³/h | 4.0/4.8 (5.5/6.6) | 4.0/5.5
300m³/h (U4.) | 5.5/6.6 (7.5/9.0) | 5.5/7.5
400m³/h (U4.) | 11.0/13.2 | 11.0/15.0
630m³/h (U4.) | 15.0/18.0 | 15.0/18.5
U5.

## Slide 40
standard motor voltages (IE3) <5.5kw
1. 3~ (Europe) 50Hz Δ-/ Y400V ± 10% (IE3) 60Hz Δ265/ Y460V ± 10% (IE3) 60Hz Δ230/ Y400V ± 10% | 2. 3~ (USA) 60Hz YY230/ Y460V ± 10% (IE3+UL/CSA) 60Hz usable @ 208V ± 10%
3. 3~ (JP/KR/BR) 50Hz Δ200/ Y350V ± 10% 60Hz Δ220/ Y380-400V ± 10% (IE3) 60Hz Δ200/ Y350V ± 10% | 4. 3~ 60Hz Δ400/ Y690V ± 10% (IE3)
U5.

## Slide 41
standard motor voltages (IE3) >5.5kw
1. 3~ (Europe) 50Hz Δ400 V/ Y- ± 10% (IE3) 60Hz Δ265 V/ Y- ± 10% (IE3) 60Hz Δ230 V/ Y- ± 10% | 2. 3~ (USA) 60Hz YY230/ Y460V ± 10% (IE3+UL/CSA) 60Hz usable @ 208V ± 10%
3. 3~ (JP/KR/BR) 50Hz Δ200/ Y350V ± 10% 60Hz Δ220/ Y380-400V ± 10% (IE3) 60Hz Δ200/ Y350V ± 10% | 4. 3~ 60Hz Δ400/ Y690V ± 10% (IE3)
U5.

## Slide 42: Thank you for your attention!